## Slide 1
Digital Logic Gates and Boolean Algebra
Part 1

## Slide 2: Introduction
Boolean Algebra: named after mathematician George Boole (1815-1864).
  Base 2 algebra
    All variables hold the literal value True (1) or False (0)
A (5v) digital circuit can have one of two values:
  Signal between 0 and 0.8 volt: 0 value
  Signal between 2 and 5 volts: 1 value
    Signal between 0.8 and 2 volts:
      undefined, gate has no deterministic output.
Gates calculate various functions of one or more input values to generate an output.
  NOT, AND, OR, XOR, etc.
Computers are made up of gates.
  Performs all logical operations
  Composed of connected transistors, resistors, capacitors, etc.
    Digital circuits

## Slide 3: Combinational Logic
Translates a set of N input variables (0 or 1) by a mapping function.
  Uses Boolean operations to produce a set of M output variables (0 or 1).

## Slide 4: Boolean Operators
Basic Operators
  AND
  OR
  NOT
Other Useful Operators
  NAND
  NOR
  XOR
  XNOR

## Slide 5: NOT Operator (Inverter)
1 goes in, 0 comes out and vice versa
Circuit:
  When input (Vin) is low, transistor turns off
  (infinite resistance) which means output
  is Vcc
    (0 in = 1 out)
  When Vin is high, transistor acts like a wire
  to ground making Vcc 0 volts.
    (1 in = 0 out)
Instant switching of states?
  Takes a few nanoseconds.

## Slide 6: NOT Operator (Inverter)
NOT truth table:
NOT gate symbol
0 | 1
1 | 0
0 | 1
1 | 0

## Slide 7: AND Operator
AND truth table:
  Output is High if all inputs are
  high.
  Otherwise, output is low.
AND gate symbol
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 8: NAND Operator
NAND truth table:
  Output is Low if all inputs are
  high.
  Otherwise, output is high.
NAND gate symbol
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 9: NAND Operator
Simplified Circuit:
  If V1 and V2 are both high, both transistors
  will conduct and produce a path to ground.
  Vout will be low (0).
  If either V1 or V2, or both, are low, the
  corresponding transistor resists, not
  allowing electricity to ground.
  Vout will be high (1).

## Slide 10: OR Operator
OR truth table:
  Output is low if all inputs are
  low.
  Otherwise, output is high.
OR gate symbol
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 11: NOR Operator
NOR truth table:
  Output is High if all inputs are
  low.
  Otherwise, output is low.
NOR gate symbol
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 12: NOR Operator
Simplified Circuit:
  If either V1 or V2, or both, are high, then transistor will conduct and produce a path to ground.
  Vout will be low (0).
  If both V1 and V2, are low, then
  both transistors resist, not allowing
  electricity to ground.
  Vout will be high (1).

## Slide 13: XOR Operator
Exclusive-OR truth table:
  Output is High if all inputs are
  mismatched.
  Otherwise, output is low.
  XOR = =
    Build this using AND, OR
    Gates?
XOR gate symbol
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 14: XNOR Operator
Exclusive-NOR truth table:
  Output is low if all inputs are
  mismatched.
  Otherwise, output is high.
  XNOR = =
    Build this using AND, OR
    Gates?
XNOR gate symbol
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
___

## Slide 15: Three Input AND Gate
A | B | C | 
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
A | B | C | 
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 16: Three Input Or Gate
A | B | C | 
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
A | B | C | 
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1